## Slide 1: BITs, Bytes & Number Systems
PDEU, Gandhinagar

## Slide 2: BIT
Bit is abbreviation of ‘Binary Digit’.
The smallest Unit in the Computer.
It can store either 0 or 1 but not both simultaneously.
i.e. they are mutually exclusive.
In computer terminology, 1 means on and 0 means off.

## Slide 3: BIT
No. of Bits | Different Combinations | No. of Different Combinations = 2No.of Bits | Highest Value stored = 2No.of Bits – 1
1 | 0 1 | 21 = 2 | 21-1 = 1
2 | 00 01 10 11 | 22 = 4 | 22-1 = 3
3 | 000 001 010 011 100 101 110 111 | 23 = 8 | 23-1 = 7

## Slide 4: Byte
The smallest unit inside the computer is bit.
However, a single bit can’t be used to store different numbers, alphabets or special symbols.
So we require a series of bits.
8 bits together makes one byte.
With one byte, we can store 256 different combinations, which include digits, alphabets and special symbols.

## Slide 5: BIT-> Tera Byte
Relationship | 
8 BITS | = 1 byte
4 BITS | = 1 Nibble
1 Byte | = 2 Nibbles
1024 Bytes | = 1 Kilo Byte (KB)
1024 KB | = 1 Mega Byte (MB)
1024 MB | = 1 Giga Byte (GB)
1024 GB | = 1 Tera Byte (TB)
Q.1. Why 1024 Bytes make 1 Kilo byte?
Q.2. What would be the highest number that
we can store, if we are having 9 bits?

## Slide 6: Different Number Systems
Decimal
Binary
Octal
Hexadecimal
ASCII
Unicode
BCD
EBCDIC

## Slide 7: Decimal Number System
Radix or Base 10
Digits 0 – 9
(153.25)10 = (1 * 102) + (5 * 101) + (3 * 100)
+ (2 * 10-1) + (5 * 10-2)
or (100 + 50 + 3 + .2 + .05)

## Slide 8: Binary Number System
Radix or Base 2
Digits 0 & 1
Conversion To Decimal
(101.11)2 = (1 * 22) + (0 * 21) + (1 * 20) + (1 * 2-1) + ( 1 * 2-2)
= (4 + 0 + 1 + .5 + .25 )
= (5.75)10

## Slide 9: Octal Number System
Radix or Base 8 (23 )
Digits 0 – 7
Conversion To Decimal
(250.14)8 = (2 * 82) + (5 * 81) + (0 * 80) + (1 * 8-1) + ( 4 * 8-2)
= (128 + 40 +0+0.125 + 0.0625 )
= (168.1875)10

## Slide 10: Hexadecimal Number System
Radix or Base 16 (24 )
Digits 0 – 9,A->10..F->15
Conversion To Decimal
(AB.75)16 =(A*161)+(B*160)+(7*16-1) +(5*16-2)
= (10*16)+(11*1)+(7/16)+(5/256)
= (171.45703125)10

## Slide 11: Decimal->Binary Conversion
(35.25)10 = (?)2
(for integer part)
Keep on dividing 35 by 2 & then take remainder from bottom to top.
(For fractional part)
Keep on multiplying .25 by 2 unless you get .00. Take digits from top to bottom.

## Slide 12: Decimal->Binary Conversion
(35.25)10 = (?)2
35
2
1
17
2
1
8
2
0
4
2
0
2
2
0
1
2
1
0
.25
* 2
--------
0 .50
* 2
---------
1 .00

## Slide 13: Decimal->Binary Conversion
(35.25)10 = (100011.01)2
35
2
1
17
2
1
8
2
0
4
2
0
2
2
0
1
2
1
0
.25
* 2
--------
0 .50
* 2
---------
1 .00

## Slide 14: Conversion: BinaryOctal
Two Ways
  Convert Binary To Decimal;
  And Decimal To Octal
  Or
  Use Direct Conversion…

## Slide 15: Direct Conversion BinaryOctal
(101110111) 2 = ( ? ) 8
Make a group of 3 bits from Right to Left. i.e. 101 110 111
Compare them with 421
4 2 1 .
1 0 1 = 5 . . ( 5 6 7 ) 8
1 1 0 = 6
1 1 1 = 7

## Slide 16: Conversion: BinaryHexa
Two Ways
  Convert Binary To Decimal;
  And Decimal To Hexa Decimal
  Or
  Use Direct Conversion…

## Slide 17: Direct Conversion BinaryHexa
(101111111) 2 = ( ? ) 16
Make a group of 4 bits from
Right to Left. i.e. 0001 0111 1111
Compare them with 8421
8 4 2 1 .
0 0 0 1 = 1 . . ( 1 7 F ) 16
0 1 1 1 = 7
1 1 1 1 = 15 i.e. F

## Slide 18: Practice Work
Convert the following:
  (1110101)2 = ( ? )8 ( ? )10 ( ? )16
  (AC0E)16 = ( ? )8 ( ? )10 ( ? )2
  (007)8 = ( ? )2 ( ? )10 ( ? )16
  (182.75)10 = ( ? )2 ( ? )16 ( ? )8

## Slide 19: ASCII
American Standard Code For Information Interchange
Most Widely Used Coding System To Represent Data.
Two Types of ASCII
  ASCII-7 (128 Diff. Combinations)
  ASCII-8 (256 Diff. Combinations)

## Slide 20: ASCII
Out of 1 byte’s 8 bits, ASCII-7 uses right most 7 bits while ASCII-8 uses all bits.
Diff. combinations includes
  10 digits ( 0 - 9 ) (ASCII values 48-57)
  26 upper case alphabets (A – Z)
    (ASCII values 65-90)
  26 lower case alphabets (a-z)
    (ASCII values 97-122)

## Slide 21: ASCII
Diff.Combinations includes
  10 digits + 52 alphabets
  Remaining are special characters and graphics characters.
To store a single character, we require one byte.
Example:
To store 153, we require 3 bytes.
  1 = 49 = 00110001
  5 = 53 = 00110101
  3 = 51 = 00110011
  = (00110001 00110101 00110011)ASCII

## Slide 22: UNICODE
Unicode defines a fully international character set from different languages.
Character set includes Latin, Greek, Arabic, Cyrillic, Hebrew, Katakana, Hangul, Hindi besides including characters from English, German, Spanish & French.

## Slide 23: UNICODE
It uses 16 bits ( 2 bytes ).
The diff. combinations are 65536.
Java uses Unicode as its number system to represent data.
1st 256 combinations are same as that of ASCII.

## Slide 24: BCD
Binary Coded Decimal
Hybrid Of Binary And Decimal
Each digit of A decimal number is converted into its 4-bit binary form
0  0000
1  0001
9  1001

## Slide 25: BCD
With 4 bits only digits can be stored. What about alphabets?
So, a new method of BCD was developed.
2 zone bits were added to 4 bits combination
  00 0000
Zone bits digit bits

## Slide 26: BCD
6 BITS i.e. 64 diff. combinations.
Includes
  10 Digits
  26 Upper Case Characters
  28 Special Characters
What about 26 Lower Case Characters?

## Slide 27: EBCDIC
Extended Binary Coded Decimal Interchange Code
Uses 4 Bits as Zone Bits
  0000 0000
Zone Bits Digit Bits
8 Bits = 256 diff. combinations

## Slide 28: EBCDIC
Includes
  10 Digits
  26 Upper Case Characters
  26 Lower Case Characters
  Rest Printable And Non-printable
  Control Characters and Special Symbols.
When we store a number, all zone bits are on i.e. 1111

## Slide 29: EBCDIC
To store 153, we require 3 bytes as under:
  1 = 1111 0001
  5 = 1111 0101
  3 = 1111 0011
  = (11110001 11110101 11110011) EBCDIC

## Slide 30: 2’s Complement Method
Most common number code for storing integer values inside the computer.
It can store signed as well as unsigned numbers.
The signs of all bits except the left most bit are +ve and the sign of leftmost bit is –ve.

## Slide 31: Drawback of 1's Complement Method
Suppose we have only 2 bits and we want to store –ve numbers also, we will have to take one bit for storing sign. 0 means number is +ve and 1 means number -ve.
0 0 = +0
0 1 = +1
1 0 = -0
1 1 = -1
The Range will be -1 to +1 as there are two representations of zero.
Sign bit
Digit Bit

## Slide 32: Drawback of 1's Complement Method
Suppose we have only 3 bits and we want to store –ve numbers also, we will have to take one bit for storing sign. 0 means number is +ve and 1 means number -ve.
0 0 0 = +0
0 1 1 = +3
1 0 0 = -0
1 1 1 = -3
The Range will be -3 to +3 as there are two representations of zero.
Sign bit
Digit Bit
Digit bit

## Slide 33: 2’s Complement Method
2(1)
-2(2)
2(0)
2
-4
1
0
0
0
0
=
1
0
1
3
=
0
1
0
-4
=

## Slide 34: 2’s Complement Method
The Range of Numbers
  -2(no.of bits-1) to +2(no.of bits-1) -1
  With 3 BITS : -4 to +3
  With 4 BITS : -8 to +7
  With 8 BITS : -128 to +127
  With 16 BITS : -32768 to +32767
  Here, only left most bit will have –ve weight.

## Slide 35: 2’s Complement Method
Convert decimal to 2’s complemented form (using 8 bits)
  107
  -107
Convert following 2’s complement numbers into decimal. (Using 8 bits)
  10001101
  01111111

## Slide 36: Binary Arithmetic-Addition
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 0 with carry 1.
Therefore, 1 + 1 + 1 = 1 with carry 1
TRY THESE:
1 0 0 0 1 0 0 1 1 0 1 1 0 1 1
+1 0 0 1 1 0 1 1 + 1 1 1 0 0 0 1
1 0 0 1 0 0 1 0 0 1 1 0 0 1 1 0 0

## Slide 37: Logic Circuits
Basic logic circuits: AND, OR, NOT
0 1
0 0 0
1 0 1
A
0 1
0 0 1
1 1 1
A
A
0 1
1 0
B
B
AND
OR
NOT
B
B
A
A
A

## Slide 38: Circuit for Addition
AND
OR
NOT
AND
A
B
S
AND
A
B
C

## Slide 39: Binary Arithmetic-Multiplication
5
×11
55
Equivalent decimal
multiplication
0101
× 1011
0101
0101
0000
0101
0110111
Binary
multiplication
Implemented in hardware using multiple
shift-left and add steps
Shift A left to multiply by B1 (= 21)
A
B
Since B2 = 0
Manual verification: 32 + 16 + 4 + 2 + 1 = 55

## Slide 40: Binary Arithmetic-Subtraction
(10101)2 – (1010) 2 = ( ? ) 2
C
1 0 1 0 1 ----> 0 1 0 1 0
- 0 1 0 1 0 -----> + 0 1 0 1 0 C
1 0 1 0 0 ----> 0 1 0 1 1
Answer: (1011) 2 Here, C means Complement

## Slide 41: Floating Point Representation
Numbers having an Integer part and a Fractional part, is called a Real Number or Floating-Point Number.
It can be either +ve or –ve.
Every number can be represented in a Scientific Form i.e. N = m r e
N=no, m=mantissa, r=radix, e=exponent

## Slide 42: Floating Point Representation
  mantissa & exponent can be
  +ve or –ve
  3.1415 = .31415 x 101
  3141.5 = .31415 x 104
  0.0031415 = .31415 x 10-2
  -31.415 = -.31415 x 102
  Note that .31415 = (3 x 10-1) + (1 x 10-2) + (4 x 10-3) +
  (1 x 10-4) + (5 x 10-5)

## Slide 43: Binary Floating Point Representation
  2-part number representation:
    Mantissa: fractional part (in binary), with sign.
    Exponent: power of 2 (in binary),
    with sign.
sign
mantissa
sign
exponent

## Slide 44: Binary Floating Point Representation
using 10 bits mantissa & 6 bits for exponent, binary +1010.001
can be represented as
0
101000100
0
00100
sign
mantissa
sign
exponent

## Slide 45: Binary Floating Point Representation
IEEE 754 Floating Point Standards
  Special codes for +/- infinity, NaN,
  +0, -0
  SINGLE PRECISION (32 BITS)
  DOUBLE PRECISION (64 BITS)

## Slide 46: Binary Floating Point Representation
IEEE 754 floating point standards
  Single Precision (32 bits)
    1 bit to store sign (left most bit)
    Exponent uses 8 bits “biased” representation
    “biased” mean adding 127 to exponent
    Exponent ranges from -126 to +127
    23 bits for mantissa
sign
exponent
mantissa
31
30………….23
22………………………0

## Slide 47: Example
(−118.625)10 = ( ? )32-BITS IEEE FORMAT
First we need to get the sign, the exponent and the fraction.
The sign will be "1" as the whole number is a negative number.
Now, we write the number (without the sign; i.e. unsigned, no two's complement) using binary notation.
The result is 1 1 1 0 1 1 0 . 1 0 1.

## Slide 48: Example
A normalized floating point number.
Next, let's move the radix point left, leaving only a 1 at its left:
1 1 1 0 1 1 0 . 1 0 1 = 1 . 1 1 0 1 1 0 1 0 1 × 26.
The first 1 binary digit is dropped.
The fraction is the part at the right of the radix point, filled with 0 on the right until we get all 23 bits.
i.e. 1 1 0 1 1 0 1 0 1 00000000000000.

## Slide 49: Example
The exponent is 6, but we need to convert it to binary and bias it (so the most negative exponent is 0, and all exponents are non-negative binary numbers).
For the 32-bit IEEE 754 format, the bias is 127
So 6 + 127 = 133.
In binary, this is written as 10000101.

## Slide 50: Example
The exponent is 6, but we need to convert it to binary and bias it (so the most negative exponent is 0, and all exponents are non-negative binary numbers).
For the 32-bit IEEE 754 format, the bias is 127
So 6 + 127 = 133.
In binary, this is written as 10000101.
1 10000101 11011010100000000000000
31 30 23 22 0

## Slide 51: Binary Floating Point Representation
IEEE 754 Floating Point Standards
  Double Precision (64 Bits)
    1 Bit To Store Sign (Left Most Bit)
    Exponent Uses 11 Bits “Biased” Representation
    “Biased” Mean Adding 1023 To Exponent
    Exponent Ranges From -1022 To +1023
    52 Bits For Mantissa
sign
exponent
mantissa
63
62………….52
51………………………0

## Slide 52: What To Use? When?
Trade-off between the range of numbers and accuracy.
If we increase the exponent bits in 32-bit format, the range can be increased but accuracy of number goes down as size of mantissa will become smaller.
Higher the no. of bits in mantissa, better will be precision.

## Slide 53: What To Use? When?
For increasing both precision and range, use double precision.
in C/C++
use float data type for single precision.
use double data type for double precision.

## Slide 54: Arithmetic on Real Nos.
Arithmetic on real numbers are more complicated.
Most ALU do only integer arithmetic
Real (floating point) arithmetic is done
  in software on some low-end processors.
  in a floating-point unit (FPU) on most modern processors.
Most processors today support single and double precision floating point arithmetic.